## Slide 1: General Purpose I/O
ENEE 3587
Microp Interfacing

## Slide 2: Memory Mapped IO Registers
IO pins, functions, control are mapped to IO registers in memory
  Simply write to or read an IO register to
    read signals from, produce signals on to pins,
    set pin functions,
    control pin operation,

## Slide 3: GPIO
Aka Ports
Used for input/output

## Slide 5
Sample from the datasheets pp 399-403

## Slide 6: Ports
8-bit IO GPIO pins
Ports A, B, C, D, E, F, G, H, J, K, L
Each port has a byte register: PORTx
  E.g. PORTA
Each port has direction register to control IO: DDRx
  E.g. DDRA byte register controls input/output function on PORTA
  Use ‘1’ for output direction, ‘0’ input
Each port has read register PINx:
  E.g. PINA
  Provides actual voltage levels on the pins (helps detect faults or read data)

## Slide 8: Configuring PORT
DDRxn: Direction register for PORT x, pin n
PORTxn: PORT x register, pin n
PUD = pull-up disable bit from register MUCR
DDRxn | PORTxn | PUD | I/O | Pull Up | Comment
0 | 0 | x | Input | No | Tri-state (Hi-Z)
0 | 1 | 1 | Input | No | Tri-state (Hi-Z)
0 | 1 | 0 | Input | Yes | PAn will source current if ext. pulled low.
1 | 0 | x | Output | No | Push-pull Zero Output
1 | 1 | x | Output | No | Push-pull One Output

## Slide 9: Examples
DDRA = 0x00; // set PortA as input with internal pull-ups on
PORTA = 0xFF;
DDRA = 0x00; // set PortA as input with internal pull-ups off
PORTA = 0x00;
DDRA = 0xFF; // set PortA for output
PORTA = 0x00;
DDRA = 0x0F; // set PortA for both input and output
PORTA = 0xF0; // upper 4 => input, lower 4 => output
DDRA = 0xAA; // set PortA for both input and output
PORTA = 0x55; // pull-ups are on

## Slide 10: PORTx vs PINx
PINxn enables access to the physical value on each Port x pin n.
Reading PORTx: Data Latch is read associated with PORT x is read
Reading PINx: the logical values present of the pins are read.
These should be the same:
  If there is a difference between the PORTxn and PINxn then the input is faulty

## Slide 11: PORT Alternate Functions
Each port also have alternate functions
  See datasheets pp 75 - 95
You must decide whether you are using port pin for GPIO or alternate functions